New Mexico Geological Society Guidebook 55, p. 19, 2004

ALTERATION SCARS IN THE RED RIVER VALLEY, TAOS COUNTY, NEW MEXICO

Virginia T. McLemore1, Virgil Lueth1, and Bruce M. Walker2

1New Mexico Bureau of Geology and Mineral Resources, New Mexico Tech. Socorro, New Mexico 87801, 2Molycorp, Inc., Questa, New Mexico 87556

More than 20 naturally forming “alteration scars”, are found along the margins of  Red River between the towns of Questa and Red River. Public and scientific interest in these scars has increased during the last decade because of sporadic but destructive mudslides or debris flows that emanate from the scar areas during wet periods (Meyer and Leonardson, 1990). In addition, water quality degradation of the Red River by the input of acid, sulfur, and other elements from surface and ground water derived from the alteration scars has been documented by recent environmental studies (Shaw et al., 2003; Briggs et al., 2003).

Alteration scars are natural, colorful (red to yellow to orange to brown), unstable landforms that are characterized by steep slopes (greater than 25 degrees), moderate to high pyrite content (typically greater than 1 percent), little or no vegetation, and extensively fractured bedrock. The scars are variable in size ranging from 1 to more than 100 acres. The distribution of the alteration scars appears to closely follow molybdenum mineralization patterns in the area. However, the relative amounts of hypogene or supergene alteration that may contribute to scar formation is yet undetermined. Many scars are located on south-facing slopes, which tend to have lower vegetation density and snow cover in winter. Erosion of the alteration scars and rapid transport out of the detritus from the source areas forms large apron-like debris fan deposits at the base of the scars. Perched ferricrete breccias are found along the margins of some scars.

Most alteration scars are composed of andesite, although other rock types are also found in some scars. The Amalia Tuff (rhyolite) forms the upper portions of some scars, especially those found high on the valley margins. The more competent rhyolite forms near vertical spires, or hoodoos at ridgelines, and are underlain by the weaker andesite and together form a badlands topography of erosion, rockfalls, slumping, landslides, and local down-slope creep of unstable ground.

Preliminary analyses of Airborne Visible-Infrared Imaging Spectrometer (AVIRIS) data indicate that the scars are characterized by abundant jarosite, kaolinite, and locally gypsum, surrounded by a halo of goethite (Livo and Clark, 2002). These secondary minerals are found in addition to common mineral phases, typical of the hypogene quartz-sericite-pyrite (QSP) altered andesite and rhyolite. Within a scar, a progression of grain size reduction is apparent. Within the scars, the rocks are fairly unaltered but highly fractured within the bottom of drainages. Progressing upward, similar in character to soil horizons, the relative sizes of clasts within the profile become smaller and the abundance of clay size material increases. Secondary mineralogies (mainly sulfates) typically cement this material during dry periods resulting in a hard surface. With prolonged wetting, this finer material becomes soft and fails readily.

The high erosion rates on the bare slopes of the scars lead to denudation that continuously exposes additional pyrite-bearing outcrops. Pyrite when exposed to water, oxidizes and forms sulfuric acid (acid drainage or AD), which then dissolves other minerals in the rock forming clay minerals and soluble sulfate, oxide, and hydroxide minerals. The dissolved constituents form acid drainage that mixes with surface and ground water and ultimately enters the Red River. Paste pH of soils in the alteration scars averages 2.5, high paste conductivities (greater than 1000 μS/cm), and sulfate concentrations ranges from 1 to 11.5 percent (Shaw et al., 2003; Robertson GeoConsultants, Inc., 2000a, 2000b, 2001). Leach extractions of samples from the alteration scars show elevated concentrations of S, Cu, F, Bi, Sn, Mn, K, and Th (Robertson GeoConsultants, Inc., 2000a, 2000b, Shaw et al., 2003).

The debris fan deposits consist of varying mixtures of interbedded fluvial, alluvial, and mudflow deposits. The buildup of these deposits in Red River reduces the river flow and results in meadows upstream of the constrictions (Meyer and Leonardson, 1990). The town of Red River, the mill, and Fawn Lakes are built upon these meadowlands.

# REFERENCES

Briggs, P. H., Sutley, S. J., and Livo, K. E., 2003, Questa baseline and pre-mining Ground Water Investigation: 11.  Geochemistry of Composited Material from Alteration Scars and Mine-Waste Piles: U. S. Geological Survey, Open-file Report 03-458, 17 p., http://pubs.usgs.gov/of/2003/ofr-03-458/.

Livo, K. E. and Clark, R. N., 2002, Mapped Minerals at Questa, New Mexico, using airborne visible-infrared imaging spectrometer (AVIRIS) data - preliminary report: U. S. Geological Survey, Open-file Report 02-0026, 13 p., http://pubs.usgs.gov/of/2002/ofr-02-0026/

Meyer, J. and Leonardson, R., 1990, Tectonic, hydrothermal, and geomorphic controls on alteration scar formation near Questa, New Mexico: New Mexico Geological Society, Guidebook 41, p. 417-422.

Robertson GeoConsultants Inc, 2001. An Integrated Geochemical Load Balance for Straight Creek, Sangre de Cristo Mountains, New Mexico. RGC Report 052008/13, January, www.molycorp.com

Robertson GeoConsultants Inc, 2000a. Interim Background Characterization Study, Questa Mine, New Mexico. RGC Report 052008/6, www.molycorp.com

Robertson GeoConsultants, Inc., 2000b, Background study data report, Questa Mine, New Mexico: Robertson GeoConsultants, Inc. Report 052008/12, January, www.molycorp.com

Shaw, S., Wels, C., Robertson, A., Fortin, S., and Walker, B., 2003, Background characterisation study of naturally occurring acid rock drainage in the Sangre de Cristo Mountains, Taos County, New Mexico; in 6th ICARD: Cairns, Queensland, Australia, July 12-18, p. 605-616, http://www.robertsongeoconsultants.com/papers/icard03back.pdf.